## Slide 1
4. 한국재료연구원

## Slide 2
Ⅱ. 기관별 연구 및 개발 계획
4. 한국재료연구원 (1/4)
초기 테스트 데이터 기반 객체 탐지 및 분류 (15장, 객체 1000개)
라벨 데이터 수령 및 학습 (2096장, 89클래스, 50만객체)
데이터 그대로 학습
클래스 축소 (비슷한 형상 맵핑)
작은 객체 제거
녹슨 정도 정량화 평가 모델 개발
이물질 탐지 모델 개발
데이터 크롭,
모델 고도화
라벨 수정, 추가데이터
재료연구원 철스크랩 관련 모델 개발 현황 요약
데이터 수령 후 순차적 학습 진행 및 모델 개선 방향 설정
추가데이터 기반 성능 향상 및 추가 모델(녹슨정도, 이물질) 개발

## Slide 3
Ⅱ. 기관별 연구 및 개발 계획
4. 한국재료연구원 (2/4)
GT
클래스 매핑
작은 객체 제거
(size 1024 기준,12px)
Chart: 
| 1.Laser cutting (thick plate) | 10.Shredded general ferrous scrap | 11.Shredder | 12.Worksite oxidized scrap | 13.Sealed drum | 14.Scrap automotive parts | 15.Gangform | 16.Chair | 18.Cut H-beam scrap | 19.Forklift truck | 2.Pipe_1 | 20.Galvanized steel pipe | 21.h-beam, i-beam, and bar- shaped steel | 22.Spring | 23.Mixed heavy iron scrap | 24.Grating manhole cover | 25.Rebar coil scrap | 26.Scaffolding pipe
Instances | 11 | 10 | 7 | 359 | 43 | 48 | 3 | 12 | 164 | 267 | 28 | 4 | 64 | 185 | 88 | 1626 | 20091 | 695
Trial 1: 데이터 전처리 X
Chart: 
| mixed steel | machine | drum | panel | trash | beam | pipe | heavy iron | mesh | structure steel | rebar | small pipe | vehicle | square pipe | Guillotine | LPG GAS cylinder | handler | plastic | Fan
Instances | 1044 | 365 | 297 | 12767 | 843 | 564 | 412 | 25851 | 20091 | 4070 | 4145 | 9231 | 575 | 335 | 870 | 328 | 12 | 2160 | 177
Trial 2: 클래스 재매핑(비슷한 형상의 객체매핑)
Chart: 
| mixed steel | machine | drum | panel | trash | beam | pipe | heavy iron | mesh | structure steel | rebar | small pipe | vehicle | square pipe | Guillotine | LPG GAS cylinder | handler | plastic | Fan
Instances | 112 | 316 | 522 | 332 | 280 | 325 | 230 | 188 | 338 | 518 | 7990 | 230 | 5 | 1933 | 2949 | 1309 | 8244 | 123 | 1709
Trial 3: 작은 객체 제거(8px)

## Slide 4
Ⅱ. 기관별 연구 및 개발 계획
4. 한국재료연구원 (3/4)
Chart: Trial 3 12px미만 객체 제거
| Box(P) | R | mAP50 | mAP50-95 | Mask(P) | R | mAP50 | mAP50-95
all | 0.778 | 0.555 | 0.641 | 0.442 | 0.748 | 0.449 | 0.502 | 0.262
Chart: Trial 1 데이터 전처리X
| Box_P | Box_R | mAP50 | mAP50-95 | Mask_P | Mask_R | Mask_mAP50 | Mask_mAP50-95
all | 0.0193 | 0.0108 | 0.0127 | 0.00722 | 0.0203 | 0.0112 | 0.0135 | 0.0101
Chart: Trial 2 클래스 매핑처리
| Box_P | Box_R | mAP50 | mAP50-95 | Mask_P | Mask_R | Mask_mAP50 | Mask_mAP50-95
all | 0.1 | 0.0622 | 0.0734 | 0.0462 | 0.087 | 0.0437 | 0.0565 | 0.0259

## Slide 5
Ⅱ. 기관별 연구 및 개발 계획
4. 한국재료연구원 (4/4)
Chart: 
| 1.Laser cutting (thick plate) | 10.Shredded general ferrous scrap | 11.Shredder | 12.Worksite oxidized scrap | 13.Sealed drum | 14.Scrap automotive parts | 15.Gangform | 16.Chair | 18.Cut H-beam scrap | 19.Forklift truck | 2.Pipe_1 | 20.Galvanized steel pipe | 21.h-beam, i-beam, and bar- shaped steel | 22.Spring | 23.Mixed heavy iron scrap | 24.Grating manhole cover | 25.Rebar coil scrap | 26.Scaffolding pipe
Instances | 11 | 10 | 7 | 359 | 43 | 48 | 3 | 12 | 164 | 267 | 28 | 4 | 64 | 185 | 88 | 1626 | 20091 | 695
*데이터셋 이슈사항
1. 클래스 불균형
2. 겹침
3. 작은 객체 다수(pipe 류)
4. 개별 / chunk 의 객체 동일 클래스 처리
5. 라벨링 오류
1
2
3
4
5